Template Fit – Summary and Results
Jonas Kasper, 08.05.2018

---
Outline
- Investigated Spectra
- Templates
- Energy model
- Fit concept
- Results:
  - Fit with two templates
  - Fit with six templates

---
Investigated Spectra
- Recorded in Cracow:
  - Series 1&3 → Fibre 1
  - Series 2&4 → Fibre 2
- Corresponding internal background measurements

---
Templates
Generated with Geant4 simulation including the shielding and the position of the source
→ one simulation for each position that was measured in the series
→ 10 templates sets

---
Templates
- Templates are:
  - P511/P1275: Photons with corresponding starting energy and interacting with photo effect in the fibre
  - C511/C1275: Photons with corresponding starting energy and interacting with Compton effect in the fibre

---
Energy Model
- Processing of the templates:
  - need to be calibrated to P.E. spectra
  - need to be smeared with a not linear resolution
- Model:
  → Bin per bin
  calibrated and
    smeared

---
Fit Concept
- Fit with two templates:
  - Internal background measurement (weight 0-1)
  - Sum of all Geant4 templates
- Fit with six templates:
  - Internal Background
  - Compton 511 keV
  - Compton 1275 keV
  - Photoeffect 511 keV
  - Photoeffect 1275 keV
  - All other energy depositions
→ Variation of energy model parameters and single fit for each combination

---
Fit Concept
- Chi² fit:
- The energy parameters are variated in:
  - parameter a in 50 steps of 0.5 around 200
  - parameter b in 20 steps of 0.01 around 0.5
  - parameter c in 20 steps of 0.01 around (taken von precali)
- Fit for each energy parameter constellation

---
Results fit with two templates
Example: spectrum with fitted templates
- Start at 70 P.E
- Simulated data not able to represent recorded spectra
- Bins with more than 10 entries taken into account

---
Results fit with two templates
Example: spectrum with fitted templates
- Start at 70 P.E
- Simulated data not able to represent recorded spectra
- Bins with more than 10 entries taken into account

---
Results fit with two templates
Template weights
IB
G4Sum
- Weights: Integral of template/Integral of sum
- Not stable for the different positions
- No matches between series 1&3 and 2&4
- Weight for IB >0.5 not reasonable

---
Results fit with two templates
Chi2/ndf distribution
Chi²/ndf with surprisingly reasonable values
Series 1
Series 2
Series 3
Series 4

---
Results fit with two templates
Energy parameter
a
- Parameter a and b not stable and the series does not fit
- Parameter c shows the expected behavior
b
c

---
Results fit with six templates
Energy resolution
- Energy resolution in the range of 7 to 10 %
- Energy resolution position dependent

---
Results fit with two templates
Energy resolution - Position dependency

---
Results fit with six templates
Example: spectrum with fitted templates
- Start at 70 P.E
- C511 totally compressed
- Bins with more than 10 entries taken into account → low entries yield to high residuals

---
Results fit with six templates
Template weights
- Weights: Integral of template/Integral of sum
- Not stable for the different positions
- No matches between series 1&3 and 2&4
- Sometimes general trends visible
IBG
EBG
P511

---
Results fit with six templates
Template weights
- Weights: Integral of template/Integral of sum
- Not stable for the different positions
- No matches between series 1&3 and 2&4
- Sometimes general trends visible
P1275
C511
C1275

---
Results fit with six templates
Chi2/ndf distribution
Chi²/ndf with reasonable values

---
Results fit with six templates
Energy parameter
- Parameter a and b not stable and the series does not fit
- Parameter c shows the expected behavior
a
b
c

---
Results fit with six templates
Energy resolution
- Energy resolution in the range of 7 to 10 %
- Energy resolution position dependent
- Behavior similar to two template fit

---
Results fit with six templates
Energy resolution -Position dependecy

---
Fazit
- Geant4 energy deposition not able to describe measurements:
  - Shielding wrong
  - Fibre material wrong
  - Pile up
- With splitting better description but still not stable results
- Energy resolution around 7-10 %